## Slide 1: Ethernet Network switch Configuration

## Slide 2: MAGNUM 6k 25 Fiber switch
Login into the Switch Through “Hi View” by entering IP Address as shown in figure:-
Enter User Id- admin & Password: “Private” (Default)

## Slide 3
Under Basic setting, go to “ system”- Here we can see which port link is up or Down & Temperature of the Switch.

## Slide 4
Under “Network” option we can set the IP Address and Subnet mask for managing the Switch.

## Slide 5
Port Type/Link status can be seen under “Basic setting >Port Configuration”. We can select auto/manual configuration.

## Slide 6
Under “Spanning Tree Global” We can SET operation in “On” and select Protocol Version as “RSTP”.
Set the priority as per the requirement. For root switch the priority will be 0(Maximum) and for 2nd Backup root switch the priority should be one step lower (ex.4096). For All other switch in the network, priority maybe kept same or One step further Lower (Ex. 8192).
Note: Inside the network, there can be a single “root switch” whose selection is done automatically by RSTP, based on Bridge priority. If the bridge priority is same, then selection is done on Lowest Mac address calculation.
Standard hello timer-2 sec., forward delay- 15 sec., Root max age- 20 sec.
Root port Mac address & Priority can be seen here.

## Slide 7
Under “Spanning Tree Port”, we can Configured the RSTP setting of Ports.
We cab also see the Port state/role status.

## Slide 8
Clarification under Help section:-
If we have manually selected “admin edge Port” by ticking the Box, then switch will treat those port as “edge port” i.e., Host/hub ied’s.
In this scenario operational port status can be seen in “Operational P2P/edge Port.”
If we have manually not selected “admin edge Port” then Switch will decide automatically “Operational P2P/edge Port.” based on the BPDU.

## Slide 9
Significance of Path Cost- There is always a cost associated bw link based on the medium of connection.
Inside the Network, Cost can be calculated in 2 ways:
1)Short method (STP-16 Bit Style)- The IEEE 802.1D specification assigns 16-bit (short) default port cost values to each port that is based on bandwidth.
2) Long method (RSTP-32 Bit style)- 802.1assigns 32-bit (long) default port cost values to each port using a formula that is based on the port bandwidth. The formula for obtaining default 32-bit port costs is to divide the bandwidth of the port by 200,000,000.
Port Speed | Default Cost Value
10 Mbps | 100
100 Mbps | 19
1 Gbps | 4
Port Speed | Default Cost Value
10 Mbps | 2000000
10 Mbps | 200000
100 Mbps | 20000
1 Gbps | 2000

## Slide 10
SNTP configuration for Time Synchronization.
External SNTP server Ip address (GPS) & Redundant SNTP Server (Aux. BCU) should be entered here.

## Slide 11
Any changes made inside switch need to be load and saved under basic settings.